PIPER PA-38-112 TOMAHAWK CHECKLISTS	Snapflight: 135.97

PREFLIGHT

Operational status

Weight & CG limits		Useful load:  582#	Payload w/full fuel: 402#

Takeoff distance			Ground roll: 820'	  	Over 50' obstacle: 1440'

In-flight performance		Max x-wind:  17 kt

Weather briefing

File flight plan

Any other factors

COCKPIT

Control wheel			release restraints

Ignition				off

Throttle				closed

Mixture				idle cut-off

Master switch			ON

Fuel gauges			check fuel level

Alternator warning light		check - on

Master switch			OFF

Primary flight controls		check for proper operation

Flaps				proper operation

Static drain			drained

Windows			clean

Baggage				stowed

Parking brake			set

Required papers			Airworthiness cert., Registration Cert, POH, placards, charts

FUSELAGE (LEFT SIDE)

General condition			check

Antennas			check

Side and rear window		Clean

Static vents			unobstructed

EMPENNAGE

Weather covers			REMOVED

General condition			check

Hinges and attachments		check

Tie down			removed and coiled

FUSELAGE (RIGHT SIDE)

General condition			check

Antennas			check

Side and rear window		Clean

Static vents			unobstructed

RIGHT WING

Weather cover			Removed

Surface condition			check - free of snow, ice, frost, etc, damage, loose screws

Flap & hinges			check (should lock when in down position)

Aileron and hinges		check (should operate smoothly)

Wing tip				check

Lights				check

Fuel color and quantity		check

Fuel cap				close and secure

Tie down			remove & coil

Chocks				remove

Brake block and tire		check

Fuel vent			check open

Fuel tank sump			drain (check for contaminants in fuel, discard sample)

NOSE

General condition			check - debris, birds nests, loose parts

Engine compartment (Right)	check

Oil				check (6 qt max,  4 qt min)

Dipstick 			seated

Alternator belt			check tension (If engine cold)

Left cowling			close and secure

Propeller and spinner		check

Air inlets			clear

Engine compartment (Left)	check

Hydraulic fluid			check

Right cowling			close and secure

Fuel strainer			drain

Switch fuel selector

Fuel strainer			drain

Nose wheel tire			check

Chocks				removed

Nose gear strut			proper inflation (>3" exposure)

Windshield			clean

LEFT WING

Weather cover			Removed

Surface condition			check - free of snow, ice, frost, other foreign matter; damage, loose parts

Stall warning			check

Fuel color and quantity		check

Fuel cap				close and secure

Tie down			remove & coil

Chocks				remove

Brake block and tire		check

Pitot head			unobstructed

Fuel vent			open

Fuel tank sump			drain (check for contaminants), discard sample2

Wing tip				check

Lights				check

Flap & hinges			check (should lock when in down position)

Aileron and hinges		check (should operate smoothly)

BEFORE STARTING ENGINE

Passenger briefing

Hobbs /Tach time			recorded

Seats				adjusted & locked

Seat belts & harnesses		fastened

Empty seat			seat belt secured

Cabin doors			closed & latched

Overhead latch			engaged

Circuit breakers			IN

Alternate static 			check

Static source			normal

ELT armed			(not sure how to check)

Brake pedal test

Avionics			off

Fuel selector			fuller tank

Carb heat			off

Anti-collision lights	 	ON

Brakes				ON

Prop				check clear

| ENGINE START | When COLD | When HOT | When FLOODED |
| --- | --- | --- | --- |
| Prime | >40F: 2 to 4 strokes, <40F: 4 + strokes; On last priming stroke, leave primer OUT | 1 to 2 strokes, On last priming stroke, leave primer OUT |  |
| Throttle | open 1/2 inch | open >1/2 inch | open FULL |
| Master switch | ON | ON | ON |
| Electric fuel pump | ON | ON | OFF |
| Mixture | full RICH | full RICH | idle cutoff |
| Starter | Engage | Engage | Engage |
| Mixture |  |  | advance |
| Primer | push in slowly after engine fires | push in slowly after engine fires |  |
| Throttle | adjust to 1000 rpm | adjust | retard |
| Oil pressure | check | check | check |
| Electric fuel pump | OFF | OFF |  |
| Fuel pressure | check | check | check |
| Primer | locked | locked |  |

WARM UP

Throttle	800 - 1200 rpm	<2 minutes in warm weather

<4 minutes in cold weather

PRE-TAXI

Flaps 			UP

Heat/Vent/Defrost	adjust

Anti-collision lights	ON

Avionics		ON

Transponder		Stby

ATIS/AWOS		UNV  127.65

Set altimeter

Set Heading Indicator

Attitude  indicator	check

Turn coordinator	check

CTAF/UNICOM		UNV  	122.8

Announce intentions	"_(insert airport name)_ traffic;  Tomahawk 2414 alpha, on the ramp, proceeding via taxiway ___ to runway ____; _(insert airport name)_traffic"

[two clicks of mic switch to ack FSS advice]

Taxi area		check clear

Parking brake		check released

foot Brakes		check

Steering			check

GROUND CHECK	At run-up area

Brakes			Set

Flight controls		check free

Trim tab		set <neutral>

Throttle		1800 rpm

Magnetos (R&L)	test (max drop 175 rpm, max dif 50 rpm)

Vacuum		5" hg +- .1

Engine gauges	check

Alternator 		test

Carb heat		set ON

Throttle		test at lowest setting (550-650 rpm)

Carb heat		set OFF

Doors/windows	check closed

Electric fuel pump	ON

Landing light 		ON

BEFORE TAKEOFF

Flight instruments	check

Master switch		check on

Carb heat		OFF or as req'd

Pitot heat		as req'd

Fuel selector		fullest tank

Mixture			set <full rich  unless high elevation>

Transponder		Alt + Sqwk 1200

Engine gauges		check

Announce intentions	"_(insert airport name)_ traffic, Tomahawk 2414 alpha, departing runway ___ to _(insert direction N/S/E/W)_ ; _(insert airport name)_ traffic"

Abort plan		ready

TAKEOFF

| NORMAL | Short field, Obstacle clearance | Short field, no obstacle | Soft field, Obstacle clearance | Soft field, no obstacle |
| --- | --- | --- | --- | --- |
| Flaps...0 | 21 (1st notch) | 21 (1st notch) | 21 (1st notch) | 21 (1st notch) |
| Release brakes Full throttle | Apply brakes Apply full power Release brakes | Apply brakes Apply full power Release brakes |  |  |
| Accelerate to 53 KIAS | Accelerate to 53 KIAS | Accelerate to 53 KIAS | Accelerate & lift nose gear ASAP. | Accelerate & lift nose gear ASAP |
| Control wheel ... Back pressure to rotate to climb attitude | Control wheel ... Back pressure to rotate to climb attitude | Control wheel ... Back pressure to rotate to climb attitude | Lift off at lowest possible airspeed. | Lift off at lowest possible airspeed. |
|  | Accelerate to 61 KIAS until obstacle clearance |  | Accelerate just above ground to 61 KIAS to climb past obstacle height |  |
|  | Accelerate to 70 KIAS after obstacle clearance | After breaking ground, Accelerate to 70 KIAS | Continue climbing while accelerating to 70 KIAS | Accelerate just above ground to 70 KIAS |
|  | Flaps ... retract slowly | Flaps ... retract slowly | Flaps ... retract slowly | Flaps ... retract slowly |

CLIMB

Best angle / shortest distance (flaps up)	61 KIAS

Best rate / shortest time (flaps up)		70 KIAS

Instruments		check

Landing light		OFF

Electric Fuel pump	OFF at desired altitude

CRUISING

Max power		75 %		2485 rpm - 6.5 gph - 94 kts

Normal power		65 %		2365 rpm - 5.8 gph - 86 kts

Economy power		55%		2225 rpm - 5.0 gph - 76 kts

Mixture			adjust, may be leaned if 75% or less power and steady cruise, else full rich

Electric fuel pump 	on when switching tanks, else off.

Heading indicator		set to compass

Carb heat		ON,  if engine RPM decreases, followed by roughness...

or Temp 20F(-7C) to 70F(21C) & Humidity 80-100%

APPROACH AND LANDING

Altimeter		set

Heading Indicator	set to compass

ATIS/AWOS		UNV  127.65

UNICOM/CTAF		UNV  122.80

Announce intentions	"_(insert airport name)_traffic, Tomahawk 2414 alpha, _(insert distance & direction)_ for downwind on runway  ____, _(insert airport name)_ traffic"

Landing lights		ON

Electric fuel pump 	ON

Carb heat		OFF

Fuel selector		fuller tank

Mixture			full RICH

Pattern altitude		UNV= 2250' MSL;  airspeed = 80 KIAS

"_(insert airport name)_ traffic, Tomahawk 2414 alpha, midfield downwind for runway ___, _(insert airport name)_ traffic"

When even with runway numbers...

Throttle			back to 1500 - 1700 rpm

Pitch up if needed to reduce airspeed

When Airspeed <89	add 1st notch Flaps

set trim 			to reduce yoke pressure

Sink rate			< 800'/min

When runway numbers at 45 degree angle over shoulder,

Check for traffic,	 right , center , left

"_(insert airport name)_ traffic, Tomahawk 2414 alpha, turning base for runway  __, _(insert airport name)_ traffic"

Turn Base

Level wings, check for traffic	 right , center, left

Flaps			full (unless winds gusting)

"_(insert airport name)_ traffic, Tomahawk 2414 alpha, turning final  for runway  __, _(insert airport name)_ traffic"

Turn Final

Airspeed		67-70 KIAS (1.3Vso)...

Throttle			add power as needed for stability

Vso . stall with flaps= 49 KIAS ... Vs. stall w/o flaps= 52 KIAS

cut power after touchdown if not Go-around,

pull back on elevator to keep nose wheel off ground

AFTER LANDING

"_(insert airport name)_ traffic, Tomahawk 2414 alpha, clear of runway  __, _(insert airport name)_ traffic"

Flaps			Up

Electric fuel pump	OFF

Strobes			OFF

Lights			as req'd

Pitot heat		Off

Transponder		Stby

SECURING

ELT			Verify silent on 121.5

Avionics		OFF

Throttle			full aft

Mixture			idle cutoff

Lights			off

Magnetos		OFF

Master switch		OFF

Hobbs/Tach time

Secure yoke with seatbelt

Chocks

Tie downs

Cabin doors

Close flight plan

# Footnotes

deleted, per Brad

added, 11/2008, dls

per POH

per Brad

If Brad, use "Little gray tomahawk";  If Jake, use "Tomahawk 2414 Alpha"

UNV pattern altitude is 2200' per AFD, 2250' per Brad